ELMET at K 2016:

ELMET will demonstrate its new high-speed dosing systems and sophisticated mold technology for liquid silicone injection molding

ELMET will present its dosing and mold technology for processing liquid silicone rubber on its own stand E49-5 in Hall 12 and additionally at ENGEL in Hall 15/C58 (2-component pressure reservoir diaphragm, top left), at MOMENTIVE in Hall 6/B15 (two-color egg cup, above center), and at BOY in Hall 13/A43 (single-wire seals, top right). Photos: © ELMET

Oftering/Austria, September 2016 – At K 2016, ELMET (www.elmet.com) will not only showcase on four different stands its new products for the injection molding of two-component liquid silicone rubbers (LSR) but will also demonstrate live a number of applications for its systems, with the machines up and running. One of the highlight on the ELMET stand in Hall 12/E49-5 will be the new multi-component dosing system TOP 5000 P for the series manufacture of demanding parts, in which ELMET has raised the bar in matters of operating comfort, safety and reliability. In addition, ENGEL, MOMENTIVE and BOY will give the company an opportunity to demonstrate its mold technology and high-performance dosing systems in action during production. To feed in the material, both ENGEL and BOY will use a TOP 3000 S dosing system from ELMET with additive control.

- At ENGEL, ELMET will show in Hall 15/C58 the production of a pressure reservoir diaphragm on a victory 160 combi multi-component injection molding machine without tie bars. After the injection of the core and frame of glass fiber-reinforced polybutylene terephthalate (Celanex 3300D from Celanese), a robot (viper 40 from ENGEL) transfers it to the LSR injection molding tools with needle valve technology from ELMET. There, a membrane of a self-adhesive, very fast-reacting silicone rubber (ELASTOSIL LR 3071/50 A/B from WACKER), is molded in place to connect the core to the frame.

- At MOMENTIVE, ELMET will demonstrate in Hall 6/B15 the production of a two-color egg cup. The interesting aspect here is the compact process of the two-component injection molding with only one dosing system on a one-component injection molding machine (ALLROUNDER 470 from ARBURG). For processing in the 4+4 cavity mold with needle valve technology and rotating core beam, the silicone (Silopren LSR 2670 from MOMENTIVE) is colored white and yellow.

- At BOY in Hall 13/A43, ELMET will demonstrate a 128-cavity LSR injection molding tool in which every cavity is directly injected by a cold runner nozzle. In this fully automatic process, which creates no production scrap, single-wire seals of silicone (Silopren LSR 3186 from MOMENTIVE) are produced on a BOY 80 E.

Wolfgang Leitner, Marketing Manager of ELMET, said: "We are delighted to have this opportunity at K 2016 to present our technology live on the production machines and with the materials of our partner companies”. The demonstrations of complete production processes under realistic conditions will give visitors an outstanding picture of the importance and functions of the individual system components required for LSR injection molding."

ELMET Elastomere Produktions- und Dienstleistungs GmbH of Oftering/Austria, established in 1996, is an internationally successful developer and manufacturer of LSR dosing systems, fully automatic injection molds, valve gate cold decks, and turnkey installations for processing silicones and rubbers. Including the staff of its ELMET North America sales and service organization, the company has some 150 staff.

Further information

Wolfgang Leitner, ELMET Elastomere Produktions- und Dienstleistungs GmbH

Tulpenstr. 21, A-4064 Oftering / Austria

Phone: +43 (0) 7221 / 74577-19
Email: w.leitner@ELMET.com

Editorial contact and voucher copies:

Dr. Jörg Wolters, Konsens PR GmbH & Co. KG

Hans-Kudlich-Str. 25, D-64823 Groß-Umstadt / Germany

Phone: +49 (0) 60 78/93 63-0, fax: -20

Email: joerg.wolters@konsens.de

This press release is available for download from: www.konsens.de/elmet.html