Recycled PET bottles:

Ettlinger’s ECO melt filters make fines almost one hundred percent recyclable

The fines which are created when PET bottles (left) are recycled contain up to 1.5% solid, gel-like or cross-linked contaminants. By incorporating Ettlinger’s ECO high performance melt filters into the extrusion process, these substances can be continuously and almost completely removed from the melt (right). © Ettlinger

Königsbrunn/Germany, June 2018 – Shredded and washed flakes are created – along with fines as the second fraction – when non-returnable PET bottles are recycled. These fines occur in large quantities and are hence a significant and valuable part of the PET cycle. However, as an input material they are difficult to handle on account of the very high proportion of paper, aluminum or PVC. The continuously operating, high performance melt filters in the Ettlinger ECO series are capable of removing high quality PET, even from such critical fractions, for subsequent reuse in the manufacture of complex products like clear thermoform sheets or packaging tape.

ECO filters are compact and can be retrofitted in existing extrusion lines without any problems. They are designed for a maximum throughput of 1000 kg/h (ECO 200) or 3000 kg/h (ECO 250) depending on the capacity requirements. The central component of these filters is a slowly rotating, cylindrical screen with millions of conical holes which is driven by a servo motor and can be supplied in a variety of sizes. When melt flows through the filter, contaminants are retained on the outside of the screen. Solid contaminants as well as gels, high-molecular and cross-linked fractions remain on the screen’s outer surface, which is continuously wiped clean by a scraper. The particles are then discharged from the unit by means of a discharge shaft, which is driven by a second servo motor. The cleaned melt on the inside of the drum is supplied to the downstream die via a system of flow channels.

The continuous cleaning principle has the advantage that blockage of the holes is avoided. This ensures a steady pressure upstream of the screen, so that no contaminants which were originally retained are inadvertently forced through the holes, impacting on the purity of the melt. Due to the extremely long interval between screen changes – several weeks or even months – in combination with the ultra-low melt losses, Ettlinger’s ECO high performance melt filters contribute to a decisive improvement in the cost efficiency of recycled PET bottles.

Ettlinger Kunststoffmaschinen GmbH was founded in 1983 and is today a global player. The German company has its headquarters in Königsbrunn, not far from Augsburg. Its core competency is the development and manufacture of high performance melt filters and injection molding machines. Ettlinger has been part of the Maag Group since 2018. 
Maag is a worldwide leading manufacturer of gear pumps, pelletizing and filtration systems and also pulverizers for sophisticated applications in the synthetic, chemical, petrochemical, pharmaceutical and food industries.

■■■

More information on Ettlinger

Karsten Bräunig, Manager Sales

Ettlinger Kunststoffmaschinen GmbH, Messerschmittring 49, D-86343 Königsbrunn

Phone: +49 8231 34908 -12, Fax: -28, e-mail: karsten.braeunig@ettlinger.com

www.ettlinger.com

Editorial contact and voucher copies:

Dr. Jörg Wolters, Konsens PR GmbH & Co. KG

Hans-Kudlich-Strasse 25, D-64823 Gross-Umstadt – www.konsens.de

Phone: +49 (0) 60 78 / 93 63 - 0, Fax: - 20, e-mail: joerg.wolters@konsens.de

Ettlinger press releases (text and pictures) can be downloaded in printable quality from: www.konsens.de/ettlinger.html